## Slide 1
GROUP 2.1
Circuit Breaker & Fuse
Selection System
A C++ application for automated load-current calculation and
protection-device recommendation
ENGINEERING PROJECT PRESENTATION

## Slide 2
Problem Statement
THE ISSUE
Incorrect breaker or fuse selection causes nuisance tripping — or, worse, serious electrical safety risks.
OUR APPROACH
Build a C++ system that calculates load current and recommends a standard protection rating automatically.
CIRCUIT BREAKER & FUSE SELECTION SYSTEM
02

## Slide 3
Aim & Objectives
AIM
Develop a C++ application that recommends suitable protection devices for a given electrical load.
OBJECTIVES
1. Calculate load and design current
2. Validate inputs
3. Recommend standard ratings
4. Save report to file
CIRCUIT BREAKER & FUSE SELECTION SYSTEM
03

## Slide 4
System Requirements
INPUTS
Circuit name
Voltage
Power
PROCESSING
I = P / V
Design Current = 1.25 × Load Current
OUTPUTS
Recommended breaker/fuse
Generated report
CIRCUIT BREAKER & FUSE SELECTION SYSTEM
04

## Slide 5
Application Features
Multiple Circuits
Handle and evaluate several circuits in one run
Input Validation
Rejects invalid or out-of-range entries
Standard Ratings
6, 10, 16, 20, 25, 32, 40, 63 A
High-Load Warning
Flags any design current above 63 A
Report Export
Saves results to protection_report.txt
CIRCUIT BREAKER & FUSE SELECTION SYSTEM
05

## Slide 6
Class Design
UML-style overview of the core C++ class
CircuitProtection
MEMBERS
CircuitName Voltage Power Load Current Design Current Rating
FUNCTIONS
setDetails()
validate()
calculate()
recommend()
display()
save()
CIRCUIT BREAKER & FUSE SELECTION SYSTEM
06

## Slide 7
Program Flow
Start
Input
Details
Validate
Calculate
Currents
Select
Rating
Display
Report
Save
File
Stop
Sequential execution — each stage completes before the next begins
CIRCUIT BREAKER & FUSE SELECTION SYSTEM
07

## Slide 8
Sample Output
Test case: 230 V, 1000 W load
LOAD CURRENT
4.35
A
DESIGN CURRENT
5.43
A
RECOMMENDED DEVICE
6
A
CIRCUIT BREAKER & FUSE SELECTION SYSTEM
08

## Slide 9
GitHub Repository Structure
Core source and documentation files
README.md
Project overview and setup instructions
main.cpp
Complete C++ source implementation
algorithm.md
Algorithm design and logic breakdown
pseudocode.md
Pseudocode reference before implementation
CIRCUIT BREAKER & FUSE SELECTION SYSTEM
09

## Slide 10
GitHub Repository Structure
Generated outputs and reporting artifacts
flowchart.png
Visual diagram of the program flow
report.md
Markdown summary of design & results
protection_report.txt
Runtime-generated recommendation report
CIRCUIT BREAKER & FUSE SELECTION SYSTEM
10

## Slide 11
Presentation & Conclusion
What we will walk through next
01
Problem Solved
02
Live Demo
03
C++ Concepts Used
04
Challenges Faced
05
Future Improvements
CIRCUIT BREAKER & FUSE SELECTION SYSTEM
11

## Slide 12
Why This Project?
Selecting the correct circuit breaker or fuse is critical for electrical safety. Our application helps users choose the correct protection device quickly and accurately.
CIRCUIT BREAKER & FUSE SELECTION SYSTEM
12

## Slide 13
Problem Solved
Calculates load current, applies a 25% safety margin, and recommends the nearest standard protection rating.
CIRCUIT BREAKER & FUSE SELECTION SYSTEM
13

## Slide 14
Real-life Use & Limitations
WHO IT HELPS
Electricians
Technicians
Students
Homeowners
LIMITATIONS
Single-phase circuits only
Fixed standard ratings
No cable sizing included
CIRCUIT BREAKER & FUSE SELECTION SYSTEM
14

## Slide 15
Future Improvements
GUI
Three-phase Support
Cable Sizing
Database
PDF Reports
Mobile / Web Versions
CIRCUIT BREAKER & FUSE SELECTION SYSTEM
15

## Slide 16
C++ Design Concepts
Language features applied throughout the implementation
Classes
Functions
Loops
Input Validation
Vectors / Arrays
File Handling
If Statements
I/O Streams
CIRCUIT BREAKER & FUSE SELECTION SYSTEM
16

## Slide 17
Thank You
Circuit Breaker & Fuse Selection System | Group 2.1